## Slide 1: An Empirical Testing of Autonomous Vehicle Simulator System for Urban Driving
John Seymour, Dac-Thanh-Chuong Ho, Quang-Hung Luu
Department of Computer Science and Software Engineering
Swinburne University of Technology, Australia

## Slide 2: Introduction
Our work presents new empirical evidence that it is feasible to
  Derive a good scenario diversity, and at the same time
  Detect AV problems in the simulation environment.

## Slide 3: questions
RQ1: Are our test cases effective in mimicking hazardous situations and can the system capture them?
RQ2: What are critical factors that distinguish a scenario to be safe or unsafe?
RQ3: Does the environmental condition have any impact on the safety of the AV?
RQ4: Is the use of simulator-based systems helpful in understanding safety in reality?

## Slide 4: TESTING Method
Equivalence Partitioning
Metamorphic Testing

## Slide 5: System under test
Apollo 6.0
SVL 2021.1

## Slide 6: Test Scenarios

## Slide 7: Test case execution & validation
Total test cases: 1062
For each scenario, we have coded a Python script and its associated Bash script to do automated testing.
For the metamorphic testing, we adopt two MRs, given a certain scenario during the daytime.
  The condition in MR1 is that the AV decision is unchanged regardless of day or night-time.
  For MR2, it requires the decision to be robust regardless of the time as well as the bad weather (intense rain and fog).

## Slide 8: 81 Tests for Scenario class A

## Slide 9: Class A – Close Quarters
AV drives between a line of parked cars, pedestrians suddenly cross its path ahead
Scenario parameters:
  General weather and time of day
  Pedestrian speed
  Pedestrian trigger distance
  Number of parked cars
  Pedestrian idle time
  Pedestrian location among parked cars
  Issues found:
  AV fails to stop in time in some circumstances and occasionally doesn’t approach slow enough

## Slide 10: Class A – Video

## Slide 11: 216 Tests for Scenario class B

## Slide 12: Class B – Pedestrian Intersection
AV makes a right turn at an intersection. Pedestrian encroaches on its right of way where it is trying to turn to.
Scenario parameters:
  General weather and time of day
  Pedestrian speed
  Pedestrian trigger distance
  Pedestrian spawn distance from curb
  Issues found:
  AV sometimes does not slow down enough before letting the pedestrian pass

## Slide 13: Class B – Video

## Slide 14: 36 Tests for Scenario class C

## Slide 15: Class C – Go around, Oncoming
AV attempts to encroach onto the other side of the road to get around a stationary NPC in its way. However, another NPC is oncoming and approaching it.
Scenario parameters:
  General weather and time of day
  Oncoming NPC speed
  Oncoming NPC trigger distance
  Oncoming NPC spawn distance
  Issues found:
  None; Ego vehicle does not ever encroach to the other side of the road, regardless of the presence of an oncoming vehicle

## Slide 16: Class C – Video

## Slide 17: 243 Tests for Scenario class D

## Slide 18: Class D – Camera Tricks
AV navigates a crowded 4-way intersection with right of way, however, two perpendicular NPC cars enter the intersection as well, encroaching into its path.
Scenario parameters:
  General weather and time of day
  Left-side NPC speed
  Left-side NPC trigger distance
  Right-side NPC speed
  Right-side NPC trigger distance
  Ego vehicle turn direction (straight ahead, left turn, right turn)
  RGB values for NPC vehicles (used for testing the camera module, if enabled in future)
  Issues found:
  AV fails to stop or even slow down in time, especially when driving straight ahead, sometimes colliding side on to an NPC
  AV sometimes collides during turns as well
  Large inconsistencies in AV behaviour for same scenario parameters

## Slide 19: Class D – Video

## Slide 20: RQ1: Are our test cases effective in mimicking hazardous situations and can the system capture them?

## Slide 21: RQ2: What are critical factors that distinguish a scenario to be safe or unsafe?

## Slide 22: RQ2: What are critical factors that distinguish a scenario to be safe or unsafe? (2)

## Slide 23: RQ3: Does the environmental condition have any impact on safety?

## Slide 24: RQ4: Is the use of simulator-based systems helpful in understanding the safety of AVs in reality?
Our study demonstrates that the effectiveness of the SVL in simulating the driving scenarios are close to human intuition.
Weather and light condition do have an impact on safety.
It is reported in our study that collisions occur in 10% of all tested scenarios, double the ratio by human driving. Considering that there are many millions of people involved in the traffic every day, this ratio is large.

## Slide 25: ANSWERS TO RQ
Answer to RQ1: The setup scenarios are effective in mimicking real-life situations; and at the same time, the system can capture collisions well.
Answer to RQ2: There are several critical factors distinguishing a scenario to be safe or unsafe.
Answer to RQ3: The environmental conditions do have an impact on the safety of AVs.
Answer to RQ4: The use of simulator-based system helps understand the safety in reality.

## Slide 26: Remarks
Our study provides a new empirical evidence to support the argument that AV simulator systems can well represent real-life scenarios.
If the system performs similarly in reality, our study implies that state-of-the-art AVs should be tested thoroughly before deployment to reduce safety-critical problems.